## Slide 1: ROS2 Basics in 5 Days Final Project
Dura Alexandru-Bogdan

## Slide 2: 1 2 3
Wall Following Behavior
- Topics -
Wall Finder - Services -
Odometry Recorder - Actions

## Slide 3: Wall Following Behavior
Subscribes to /scan topic to get lidar data
Publishes Twist messages into /cmd_vel topic to control the robot.
If messages from /scan shows object detected in front closer than 0.5 => turn fast left while going ahead
If mesages from /scan shows object detected on the right closer than 0.25 => turn slightly left while going ahead.
If mesages from /scan shows object detected on the right at distance over 0.3 => turn slightly right while going ahead.

## Slide 4: Wall Finder Behavior
Subscribes to /scan topic to get lidar data
Publishes Twist messages into /cmd_vel topic to control the robot.
Creates service /find_wall
Turns the robot till the lowest value is for the front facing lidar ray
Moves to the wall till the distance of the front ray is 0.3cm
Turns the robot till the lowest value is for the right facing lidar ray

## Slide 5: Odometry Recorder
Subscribes to /odom topic to get odometry data
Calculates the distance from the start point till the position of the robot based on the data from /odom.
If the distance from the start is lower than 0.2 it means that the robot completed a lap and sends the odometry data recorded
Every one second the distance between the past and present positions is calculated and all point are appended to a list. This distance is added to the current_distance on each step.

## Slide 6: THANK YOU!